## Slide 1: Next Generation AI for Power Electronics: Explainable, Light, and Flexible
Organizer: Dehong Xu, Homer Alan Mantooth
Speaker: Xinze Li, Fanfan Lin, Huai Wang, Xin Zhang

## Slide 2: Section I. Applications of AI in Power Electronics
Speaker: Xin Zhang, Huai Wang

## Slide 3: Applications of AI in Power Electronics
I
Applications of AI in Power Electronics
Source: Shuai Zhao, Frede Blaabjerg, and Huai Wang, “An overview of artificial intelligence applications for power electronics,” IEEE Transactions on Power Electronics, vol. 36, no. 4, pp. 4633 – 4658, Apr. 2021.
Xin Zhang, Huai Wang

## Slide 4: Applications of AI in Power Electronics
I
Percentage of AI Tasks in Power Electronics
Source: Shuai Zhao, Frede Blaabjerg, and Huai Wang, “An overview of artificial intelligence applications for power electronics,” IEEE Transactions on Power Electronics, vol. 36, no. 4, pp. 4633 – 4658, Apr. 2021.
Percentage in the existing research work
9.8% for Design
77.8% for Control
12.4% for Maintenance and Fault Diagnosis
Xin Zhang, Huai Wang

## Slide 5: Applications of AI in Power Electronics
I
Timeline of AI Algorithms Applied in Power Electronics
Just like plant grafting, where a specific branch is carefully chosen and integrated into a compatible rootstock
AI needs to be adapted and enhanced with power electronics expertise.
Xin Zhang, Huai Wang

## Slide 6: Applications of AI in Power Electronics Design
I
Existing Application 1: AI-Based Circuit and Control Design
Abstract diagram of circuit and control design through AI-based methods
Xin Zhang, Huai Wang

## Slide 7: Applications of AI in Power Electronics Design
I
Data collection
Outlier exclusion
Data-driven digital model
Meta-heuristic optimization
Hardware experiments
AI-in-Loop System for Modulation Design of DAB Converters
AI-based data-driven modeling
Meta-heuristic algorithm
Residual models to deal with model deviation
Fuzzy logic for online deployment
②
③
④
Support vector machine
①
y = fML (x)
AI-empowered Model-Based Design to streamline modeling, optimization, and design iteration
Source: X. Li, X. Zhang, F. Lin, C. Sun and K. Mao, "Artificial-Intelligence-Based Triple Phase Shift Modulation for Dual Active Bridge Converter With Minimized Current Stress," in IEEE Journal of Emerging and Selected Topics in Power Electronics, vol. 11, no. 4, pp. 4430-4441, Aug. 2023.
X. Li et al., "Data-Driven Modeling With Experimental Augmentation for the Modulation Strategy of the Dual-Active-Bridge Converter," in IEEE Transactions on Industrial Electronics, vol. 71, no. 3, pp. 2626-2637, March 2024
Xin Zhang, Huai Wang

## Slide 8: Applications of AI in Converter Condition Monitoring
I
Existing Application 2: Digital Twin Based Condition Monitoring
Huai Wang, Xin Zhang
Source: S. Zhao, Y. Peng, Y. Zhang and H. Wang, "Parameter Estimation of Power Electronic Converters With Physics-Informed Machine Learning," in IEEE Transactions on Power Electronics, vol. 37, no. 10, pp. 11567-11578, Oct. 2022.

## Slide 9: Applications of AI in Converter Condition Monitoring
I
Digital twin models share the same operational characteristics and internal device parameters as their physical counterparts.
High-precision digital twin models can be used for real-time system optimization, health assessment, device performance prediction, and more.
Circuit parameters
Source: S. Zhao, Y. Peng, Y. Zhang and H. Wang, "Parameter Estimation of Power Electronic Converters With Physics-Informed Machine Learning," in IEEE Transactions on Power Electronics, vol. 37, no. 10, pp. 11567-11578, Oct. 2022.
Huai Wang, Xin Zhang
Existing Application 2: Digital Twin Based Condition Monitoring

## Slide 10: Applications of AI in Converter Condition Monitoring
I
System Digital Twin Model: Circuit Model, Control, Sampling
Existing Application 2: Digital Twin Based Condition Monitoring
Schematic diagram of AI-based digital twin
Huai Wang, Xin Zhang

## Slide 11: Applications of AI in Converter Condition Monitoring
I
Meta-Heuristic Optimizer, e.g.
Particle Swarm Optimization (PSO）
No additional hardware required.
No calibration needed.
Converter-level condition monitoring solution, capable of monitoring multiple devices simultaneously.
Parameter identification algorithm
Existing Application 2: Digital Twin Based Condition Monitoring
Huai Wang, Xin Zhang

## Slide 12: Challenges of Existing AI in Power Electronics
I
Challenge 1: Power Electronics Requires Data-Light and Computation-Light AI
Characteristics of power electronics and other fields
Source: Aalborg University, “Researchers will design cognitive power electronics”,
https://www.aau.dk/researchers-will-design-cognitive-power-electronics-n28286
Huai Wang, Xin Zhang

## Slide 13: Challenges of Existing AI in Power Electronics
I
The inductor helps to smooth out the ripple in the output current by resisting sudden changes in current flow. Lower ripple percentages typically require larger inductors.
AI:
For the task to design LC filter for the buck converter which has minimum current ripple, why do you recommend this inductor value?
User:
Source: https://towardsdatascience.com/need-for-explainability-in-ai-and-robotics-75dc6077c9fa;
F. Lin et al., "PE-GPT: A New Paradigm for Power Electronics Design," in IEEE Transactions on Industrial Electronics, doi: 10.1109/TIE.2024.3454408.
Leverage PE-GPT to Provide Power Electronics Insights into a Designed Buck Converter
PE-GPT by F. Lin et al.
Challenge 2: Explainability of AI to Enhance Deployment Confidence
Huai Wang, Xin Zhang

## Slide 14: Challenges of Existing AI in Power Electronics
I
Traditional data-driven is fixed in operational settings, limiting model flexibility when settings change.
Building separate surrogate models for all settings is data-intensive and computationally demanding.
Handling multiple settings need Nt​=m×n×z models (imaging only 3 variables), increasing complexity significantly.
Topology, circuit parameters, control strategies, performance metrics, operation specifications, etc., could all change.
Challenge 3: Flexibility for Diverse Converters and Operating Conditions
Number of models required for variable modulation strategy, operation specification, and performance metrics
Huai Wang, Xin Zhang

## Slide 15: Section II. Physics-Informed Machine Learning (PIML) for Power Electronics
Speaker: Xinze Li

## Slide 16: Concept of Physics-Informed Machine Learning
Concept of Physics-Informed Machine Learning (PIML):
II
Forward Problem (Solve PDEs)
Inverse Problem (Infer Parameters)
Source: G. E. Karniadakis, I. G. Kevrekidis, L. Lu, P. Perdikaris, S. Wang, and L. Yang, “Physics-informed machine learning,” Nat Rev Phys, vol. 3, no. 6, pp. 422–440, May 2021, doi: 10.1038/s42254-021-00314-5
Integrate physics
Physics Laws Expressed as Partial Differential Equations (PDEs)
Machine Learning Models
Steer the learning of PIML towards identifying physically consistent solutions
Ill-posed scenarios
  Noisy or missing data
  Deficient physical models
Mesh-free
Easy mathematical formulation
Rich support in AI fields
Identify parameters
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 17: How to Embed Physics into Machine Learning
Main Types of PIML Approaches:
II
Physics-in-Loss PIML
Physics-in-Architecture PIML
Physics-in-Initialization PIML
Physics is embedded into loss terms for training
Introducing learning biases
Physics is embedded directly into neural structure
Introducing inductive biases
Initialize neural weights for physically informed starting points
Reveal data invariant
Adjust prior distribution
Most widely applied
Focus of this Session
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 18: Physics-in-Loss PIML
Physics-in-Loss PIML and Some Applications:
II
Source: G. E. Karniadakis, I. G. Kevrekidis, L. Lu, P. Perdikaris, S. Wang, and L. Yang, “Physics-informed machine learning,” Nat Rev Phys, vol. 3, no. 6, pp. 422–440, May 2021.
S. Zhao, Y. Peng, Y. Zhang, and H. Wang, “Parameter Estimation of Power Electronic Converters With Physics-Informed Machine Learning,” IEEE Transactions on Power Electronics, vol. 37, no. 10, pp. 11567–11578, Oct. 2022.
Physics as PDEs:
Loss Terms
AutoDiff
Solve PDEs with partially hidden physics
Parameter identification for power converters
Identify
Data acquisition
Circuit parameters
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 19: Physics-in-Architecture and Physics-in-Initialization
Physics-in-Architecture and Physics-in-Initialization PIMLs
II
Physics as PDEs
Discretization with numerical differentiation
Steer the Physics-Crafted Structural Design of ML
Neural parameters θ are endowed with direct physical meanings
θ
Physics as PDEs
Randomly initialized with small weights (Xavier Initialization)
Conventional ML Models
Initialize neural parameters to meet certain physical constraints
Xinze Li, Fanfan Lin, Homer Alan Mantooth
Physics-in-architecture
Physics-in-initialization

## Slide 20: Pros and Cons of Main PIML Methods
Pros and Cons of Main PIML Methods:
II
Data Requirements
Physics-in-Architecture
Physics-in-Loss
Less Data
More Lightweight
More Flexible
More Explainable
Many Physics
Some Physics
NO Physics
Few Data
Some Data
Massive Data
Stronger Data-Driven Capacity
Physics Effectiveness
Purely Data-Driven
Low data-driven capacity
Limited to simpler physical formulation
Disadvantages
Physics inconsistent
Necessitate re-train for out-of-domain scenarios
More training epochs
No physical meaning
Massive data needed
Black-box and heavy model
~ 100 to 101
~ 102 to 103
≥ 104
NO
Allow for Hidden Physics
Well-Posed
Xinze Li, Fanfan Lin, Homer Alan Mantooth
Physics-in-Init.

## Slide 21: Section III. Fundamentals of PANN and its Explainability in Power Electronics
Speaker: Xinze Li

## Slide 22: Introducing PANN: Next-Generation of AI for PE
Neural weights A ~ D have NO physical meanings
Concept of PANN: Physics-in-Architecture Neural Network (PANN)
III
Source: [1] X. Li et al., "Temporal Modeling for Power Converters With Physics-in-Architecture Recurrent Neural Network," in IEEE Transactions on Industrial Electronics, vol. 71, no. 11, pp. 14111-14123, Nov. 2024.
[2] X. Li, F. Lin, X. Zhang, H. Ma and F. Blaabjerg, "Data-Light Physics-Informed Modeling for the Modulation Optimization of a Dual-Active-Bridge Converter," in IEEE Transactions on Power Electronics, vol. 39, no. 7, pp. 8770-8785, July 2024.
[3] F. Lin, X. Li, X. Zhang and H. Ma, "STAR: One-Stop Optimization for Dual-Active-Bridge Converter With Robustness to Operational Diversity," in IEEE Journal of Emerging and Selected Topics in Power Electronics, vol. 12, no. 3, pp. 2758-2773, June 2024.
[4] X. Li et al., "A Generic Modeling Approach for Dual-Active-Bridge Converter Family via Topology Transferrable Networks," in IEEE Transactions on Industrial Electronics, doi: 10.1109/TIE.2024.3406858.
[5] F. Lin et al., "PE-GPT: A New Paradigm for Power Electronics Design," in IEEE Transactions on Industrial Electronics, doi: 10.1109/TIE.2024.3454408.
Mamba State Space Models (Submitted on 1 Dec 2023)
Physics-in-Architecture Neural Network (PANN)
(Submitted on 21 Jun 2023)
All roads lead to destination, but PANN is a Shortcut for PE
Embed PE physics in PDEs, neural θ denotes circuit parameters
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 23: Why PANN? Explainable! Light! Flexible!
III
Explainable
Physics-crafted architecture through discretized state-space circuit equations
Power electronics explainable
  Switching behaviors
  Commutation loops
Light
Data-light
  Reduce data by 3 orders of magnitudes
  Countable in one hand
Lightweight
  Deployable on edge
  Down to kB level
Flexible
Training-free to out-of-domain scenarios
  Operating conditions
  Modulation strategies
  Performance metrics
  Circuit parameters
  Topological variants
PANN is Suitable for Power Electronics Applications
Advantages of PANN: Explainable, Light, and Flexible
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 24: Network Architecture and Principles of PANN
PANN is a form of Neural Partial Differential Equations (NeuralPDE)
III
Trainable neural parameters, data-driven
Generic state-space equations of power converters
Continuous
Discrete
Physically explainable, direct assignment
Expert Systems
Recurrent neural architecture of PANN
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 25: PANN Inference: Predict the Next State
PANN inference unfolded over time: predict the next state
III
Predicted state x[tk+1] at tk+1 is used to infer the following state x[tk+2] at tk+2
Used as next
unfolded
In modeling, teacher forcing is infeasible
x[tk+1]
x[tk]
Physics-in-Architecture
Implicit Cell
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 26: PANN Inference: Predict the Next State
PANN inference unfolded over time: predict the next state
III
Time tk+1
Time tk
Time tk+2
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 27: Code Structure for PANN Inference
III
Module 2. Input Blocks
Generate switching or input signals based on modulation knowledge
Code Structure for PANN Inference
Module 3. Physics Cell
Infer state variables for one timestamp based on physics
Module 1. Recurrence Cell
Infer state variable waveforms in a recurrent way
PANN Inference
..., u[tk], u[tk+1], ...,
x[tk]
x[tk+1]
Module 1. Recurrence Cell
pann_net.py :: class PANN
Physics Cell
Recurrent Inference
Recurrent infer
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 28: Case Study: PANN for DAB Converters
Case Study 1: PANN for DAB Converters
III
Equivalent Circuit of Inductor
Continuous
Discretize via Implicit Euler Algorithm
Simplify
PANN Structure for DAB
 | Specs
States x(t) | iL
Inputs u(t) | vp, vs
Circuit θ | RL, Lk, n
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 29: Case Study: PANN for DAB Converters
Case Study 1: PANN for DAB Converters
III
Module 2. Input Blocks
pann_utils.py :: def create_vpvs
To generate vp and vs
Gate drive signal for s1
Gate drive signal for s4
Gate drive signal for s5
Gate drive signal for s8
Generate vp and vs
Exemplary vp and vs waveforms
args: (D0, D1, D2, D1_cycle, D2_cycle, vi, vo)
return:
args: (0.1, 0.7, 0.95, 50%, 50%, 200, 160)
embed
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 30: Case Study: PANN for DAB Converters
Case Study 1: PANN for DAB Converters
III
Module 3. Physics Cell
pann_net.py :: class EulerCell_DAB
Inference Breakdown (Code Demo*)
"DAB-inference and training.ipynb"
Define neural circuit parameters θ
Physics of inductor
Animated inference breakdown
Expert system
vp
vs
iL
.
.
.
.
.
.
tk
tk+1
tk+2
Embed physics
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 31: Next-Generation of Explainable AI for Power Electronics
III
Circuit Insights Revealed in PANN
Expert system
Switching behaviors
Commutation loop analysis
PANN pushes the definition of AI explainability to a NEW Height: Power Electronics Explainable
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 32: Exemplary Waveforms of PANN Inference for DAB
III
Exemplary waveforms of PANN for DAB
A DAB Variant (NPC-DAB) under TPS Modulation
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 33: Case Study: PANN for Buck Converters
Case Study 2: PANN for Buck Converters
III
 | Specs
States x(t) | iL, vo
Inputs u(t) | va
Circuit θ | R, L, C
Equivalent Circuit
Continuous
Discretize via Explict Euler Algorithm
Simplify
PANN Structure for Buck
s[tk]vi
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 34: Case Study: PANN for Buck Converters
III
Module 3. Physics Cell
pann_net.py :: class EulerCell_Buck
Inference Breakdown (Code Demo*)
“Buck-inference.ipynb"
Physics of capacitor
Case Study 2: PANN for Buck Converters
Physics of inductor
Determine DCM
Embed physics
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 35: Next-Generation of Explainable AI for Power Electronics
Circuit Insights Revealed in PANN
III
Expert system
Switching behaviors
Commutation loop analysis
PANN pushes the definition of AI explainability to a NEW Height: Power Electronics Explainable
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 36: Key Takeaways of PANN Inference
III
PANN Inference
Takeaways
Equivalent circuit
Define states, inputs, outputs variables
Continuous state-space circuit equations
Discretized state-space
Construct PANN
Neural ODE/PDE
Time-domain modeling
Present predictions are used to predict next states
Infer state variables x(t) based on input variables u(t) from expert systems
I. Recurrence Cell
II. Input Blocks
Loop through timestamps
Numerical
III. Physics Cell
Generate Input Signals
Embed Physics
Physics-crafted structure: state-space circuit physics
Physical compliance
Explainability in power electronics: switching behaviors, commutation loops, operating modes
Xinze Li, Fanfan Lin, Homer Alan Mantooth
1. To Customize PANN for ANY Power Converter
3. Main Features of PANN Inference
2.
Code Structure of PANN
4.
Explain-ability of PANN

## Slide 37: Section IV. PANN is Light in Two Aspects: Data-Light and Lightweight
Speaker: Xinze Li

## Slide 38: PANN Training: Adjust Neural Parameters to Minimize Loss
Training is Imperative to minimize losses
IV
After Proper Training
Before Training
Neural θ before Training: RL = 10 mΩ, Lk = 80 μH, n = 1.1
Neural θ after Training: RL = 1.8 Ω, Lk = 64 μH, n = 1.0
Manufacturing tolerance
Ambient variations
  Thermal drift
  Operation conditions
  Electromagnetic interference
Aging and degradation
R2 = 96.9%
R2 = 99.9%
Deviated theoretical modeling
With Training
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 39: PANN Training: Flowchart and Breakdown
PANN training breakdown
IV
Training Breakdown
PANN with current neural parameters θ
u[tk], x[tk]
x[tk+1]
θ
infer
expressed as tensors
update θ
Training Flowchart of PANN
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 40: Training Loop of PANN
IV
ONE Epoch of PANN Training
Loaded training data
New epoch
Data Loader
torch.utils.data.DataLoader
PANN Inference
Input Blocks in pann_utils.py
Recurrent Cell and Physics Cell defined in pann_net.py
Predicted state waveforms
Loss Function
Various losses in torch.nn
Evaluated loss & computational graph
Update Neural Parameters θ
torch.optim
Backpropagation
WeightClamp defined in pann_net.py
Evaluate Test Loss
Similar to PANN Inference, but without recording gradients
Updated PANN
Save checkpoint
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 41: PANN Training Code Analysis
IV
Main Loop of PANN Training
pann_train.py :: def train
Define a clamper of class WeightClamp
Bound the weight during training to avoid unrealistic neural θ
PANN Inference
Define an optimizer with different learning rates for neural θ
Evaluate Loss
Backpropagate Loss
Clamp Neural Parameters θ
Defined in
Defined in
Define training process
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 42: Case Study: PANN Training of DAB
IV
PANN Training (Code Demo*, "DAB-inference and training.ipynb")
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 43: Case Study: PANN Training of DAB
IV
PANN Training (Code Demo*, "DAB-inference and training.ipynb")
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 44: Tuning of Learning Rates for PANN Training
Tuning of learning rates
IV
Training Curves
Training Performances w.r.t. Learning Rates
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 45: Next-Generation of Light AI for Power Electronics
PANN is Lightweight.
IV
MAEs / A (mean±std.) | Data Sizes for (Train, Test, Validation) Sets |  | 
 | (10, 90, 900) | (50, 90, 860) | (100, 90, 810)
Piecewise | 0.311±0 |  | 
SVR | 2.286±0 | 2.052±0 | 1.991±0
LSTM | 1.560±9.5E-2 | 1.340±5.6E-2 | 1.193±9.9E-2
TCN | 1.371±3.6E-1 | 0.726±6.1E-2 | 0.511±7.2E-2
PL-PINN | 0.310±1.3E-2 | 0.259±1.1E-2 | 0.234±7.3E-3
LN-GRU | 1.257±1.2E-1 | 0.991±1.2E-1 | 0.527±8.6E-2
PANN | 0.160±4.1E-3 | 0.145±3.6E-3 | 0.132±3.3E-3
PANN is Data-Light.
PANN pioneers the next-generation of LIGHT AI for power electronics in:
1. Data: countable on ONE HAND, 2. Model size: deployable on EDGE DEVICE.
Data Size
≥
#Params.
Embed Data Invariant
Popular ML: Thousands, Millions, and MORE
PANN: a handful of data, reducing by 3 orders of magnitudes
PE Physics
PANN Visualizer
1.72 kB of a PANN for DAB
Deployable on Edge
Raspberry pi
TMS320
STM32
Xilinx fpga
Arduino
1762 strings,
Approx. 160 words
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 46: Key Takeaways of PANN Training
IV
PANN Training
Takeaways
Xinze Li, Fanfan Lin, Homer Alan Mantooth
1.
Training Flowchart of PANN
Training of PANN
Dataset division
Hyperparameter tuning
Load model checkpoint
Validate PANN
2.
Training Loop of PANN
PANN Inference
Load training data
Evaluate training loss
Update neural θ: backpropagate & clamp
Evaluate test loss
4.
PANN is a “Light“ AI Model
Data-light: training data required for PANN is countable on ONE HAND
Lightweight: few kBytes, deployable on resource-constrained EDGE devices
3. Hyper-Parameter Tuning of PANN
Learning rates lr of PANN should be carefully tuned
Low lr: slow convergence
High lr: large oscillation
Rule of thumb: lr to be 1% of parameter values

## Slide 47: Section V. PANN is Flexible: “All You Need” is One PANN Model
Speaker: Xinze Li

## Slide 48: PANN – Next Level of Flexibility: Training-Free
V
Total Number of Conventional ML Models required:
MS×PM×OS×TP
ONE PANN for Diverse Conditions and Topologies
Four Angles of PANN’s Flexibility
01
02
03
04
Operating Conditions
Circuit Parameter & Topology
Performance Metrics
Modulation Strategy
PANN’s Flexibility
Training-FREE
vi
vo
PL, etc.
PSM
PWM
Hybrid
Lk
RL
n, etc.
Non-resonant
Resonant
Multi-port
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 49: PANN – Flexibility across Conditions
Flexibility across Conditions - DAB
V
Code Implementation
Adjust the Knowledge in Input Blocks
Flexibility 1: Out-of-Domain Operating Conditions
Flexibility 2: Diverse Modulation Strategies
Adjust Expert System
Adjust expert system
Adjust vi and vo
Adjust expert system
Adjust duty cycles
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 50: Case Study: PANN’s Flexibility across Conditions
V
PANN’s Flexibility across Conditions (Code Demo*, "DAB-Operational Transfer.ipynb")
Source: vi = 200 V; vo [160 V, 240 V]
Target: vi = 300 V; vo
Target: vi = 300 V; vo
Source: TPS Modulation
Target: vi = 200 V; vo
D1_cycle = 50%, D2_cycle = 35%
Target: vi = 200 V; vo
D1_cycle = 68%, D2_cycle = 50%
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 51: PANN – Flexibility across Performance Metrics
V
Flexibility across Performance Metrics - DAB
Flexibility 3: Various Performance Metrics
One-Stop Metric Adapter for Diverse Performances
ZVS turning-on
Current stress
ipp = iL,max-iL,min
Reactive power
Q = vL,rms·iL,rms
Conduction loss
Transferred power
Circulating current, etc.
Code Implementation
star_metric_adapter.py
Primary ZVS
Locate switching timestamp
Peak-peak current
RMS current
Secondary ZVS
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 52: PANN – Flexibility across Circuit Parameters
V
Flexibility across Different Circuit Parameters by Training or Direct θ Assignment
Code Implementation
Adjust Neural θ in Physics Cell Module
Directly assign new circuit parameters to neural θ
Flexibility across Circuit Parameters - DAB
Training
Direct Assignment Training-Free
Circuit Parameter Transfer (Code Demo*)
"DAB-Operational Transfer.ipynb"
source: RL = 120 mΩ; Lk = 63 μH; n = 1
target: RL = 120 mΩ; Lk = 6.3 μH; n = 1
source
target
Flexibility 4-1: Different Circuit Parameters
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 53: PANN – Flexibility across Topologies
V
Flexibility across Topologies - DAB Family
Topology Transfer between Non-Resonant and Resonant DAB
Discretized by Implicit Euler:
Added physics of vC of resonant capacitor
vC is added into the voltage loop
Discretized by Implicit Euler:
Add Branch
Delete Branch
Flexibility 4-2: Different Topological Variants
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 54: PANN – Flexibility across Topologies
Topology Transfer between Non-Resonant and Resonant DAB
V
PANN’s Neural Link Transformation
Code Implementation
DAB-Topology Transfer.ipynb
Non-resonant DAB with Single L
Added State
Add vC into the voltage loop
Add physics of vC
Resonant DAB with Series LC
Add vc into voltage loop
Add physics of vc
Schematic Diagram of PANN for Topology Transfer
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 55: Case Study: PANN’s Flexibility across Topologies
V
PANN’s Flexibility across Topologies (Code Demo*, "DAB-Topology Transfer.ipynb")
Source: Non-resonant DAB with Single L, Lk = 63 μH
Target: Lr = 63 μH, fr = 1.1·fs (Capacitive)
Target: Lr = 63 μH, fr = 0.9·fs (Inductive)
Target: Lr = 63 μH, fr = 1.0·fs (Resistive)
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 56: Statistical Study of PANN’s Flexibility
Flexibility across Conditions and Modulations
V
Data Partition Settings to Validate Flexibility across Conditions
Statistics of Condition Transferability
Statistics of Modulation Transferability
R2=99.68%
R2=99.75%
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 57: Statistical Study of PANN’s Flexibility
Flexibility across Performance Metrics and Modulations
V
Statistics of Performance Transferability
Waveforms of Topology Transferability - LC
R2=99.66%
R2=99.79%
Waveforms of Topology Transferability - TAB
Statistics of Topology Transferability
Xinze Li, Fanfan Lin, Homer Alan Mantooth

## Slide 58: Key Takeaways of PANN’s Flexibility
IV
PANN’s Flexibility
Takeaways
Xinze Li, Fanfan Lin, Homer Alan Mantooth
Flexibility I.
Operating Conditions
Simply update operating params. in expert system to change input signals
Training-free
Flexibility II.
Modulation Strategy
Switching behaviors in expert system should be updated accordingly
Training-free
Flexibility III.
Performance Metrics
Numerically gauge metrics based on input signals from expert system and state waveforms from PANN
Metric adapter is case-specific, rely on topology, modulation, etc.
Training-free
Flexibility IV.
Circuit Parameters & Topology
Circuit θ is adjustable if there is: 1) training data; 2) priori knowledge of θ (direct value assignment)
Topology transfer: add/del. neural links of PANN

## Slide 59: Section VI. Future Directions of PANN in Power Electronics
Speaker: Fanfan Lin

## Slide 60: Future Directions of PANN in Power Electronics
VI
Health Monitoring
Predictive Maintenance
More nuanced, accurate, and comprehensive PANN
Model-based Design
Co-design of topology, circuit, and control
Hybrid data-driven and physics-based modeling
Design Automation
PANN in PE
More topologies
Adaptive Control
Adaptive Diagnosis
Design
Control
Maintenance
PANN in the Life Cycle of Power Electronics Systems
Fanfan Lin, Xinze Li

## Slide 61: Future Directions of PANN in Power Electronics
VI
I. PE Design Automation
Source: F. Lin et al., "PE-GPT: A New Paradigm for Power Electronics Design," in IEEE Trans. on Ind. Electron.
Code: https://github.com/XinzeLee/PE-GPT
Optimal design insights
Modeling and optimization
Training of PANN
PE-GPT: Large language model-based framework for PE design
Enhance Model Zoo
More nuanced and comprehensive PANN
PANN models for more converter topologies
Improve modeling accuracy
Fanfan Lin, Xinze Li

## Slide 62: Future Directions of PANN in Power Electronics
VI
II. Adaptive Control
PANN
III. Health Monitoring
Sampling
Online training
Edge Device
Collected Datasets
Digital Twin
PANN with updated neural param. θ
COM
Represent
Continuously update PANN for online monitoring
Converter behaviors
Predict
Update
Minimize the cost function:
Predicted {y[tk]}k, {x[tk]}k
Train
Fanfan Lin, Xinze Li

## Slide 63: Conclusions
VI
Fanfan Lin, Xinze Li
AI algorithms applied in PE require explainable, light, and flexible solutions
Conclusions
PIML introduces physics expressed as PDEs into ML models to steer learning towards identifying physically consistent solutions
PIMLs can solve PDEs in forward ways and identify parameters in inverse settings
PIMLs are effective for ill-posed and mesh-free forward problems to solve PDEs and inverse problems to identify parameters.
Three types of PIMLs: Physics-in-loss, physics-in-architecture, physics-in-initialization
Physically crafted recurrent networks to integrate PDEs discretized by numerical methods
PANN features time-domain modeling for power electronics, where state variables are recurrently predicted leveraging the previous predictions of states
PANN is explainable in PE: Neural parameters of PANN are converter parameters, and switching behaviors, commutation loops, operating modes and so on are embodied
Training only requires few data samples, reducing data requirements by 3 orders of magnitude
PANN is lightweight (several kB), deployable on edge devices
PANN training equals to parameter identification, and learning rates are impactful hyperparameters
Flexible across operating conditions, modulation strategies, performance metrics, circuit parameters, and topological variants
Training-free transfer (use knowledge to replace data)
Apply PANN in design automation, adaptive control, and health monitoring for power converters
More nuanced, accurate, and comprehensive PANN to incorporate more topologies
PIML
Explain-able
Flexible
Light
Future
PANN

## Slide 64: Thank you! Q&A
Organizer: Dehong Xu, Homer Alan Mantooth
Speaker: Xinze Li, xinzel@uark.edu
Fanfan Lin, fanfanlin@intl.zju.edu.cn
Huai Wang, hwa@energy.aau.dk
Xin Zhang, zhangxin_ieee@zju.edu.cn
2024 Nobel Prize - Physics
Awarded to AI Pioneers
Next-Generation of AI for Power Electronics
The ultimate frontier of AI is physics-informed AI.